## Slide 1: Add a modular heat pump approach #1576
https://github.com/ibpsa/modelica-ibpsa/issues/1576

## Slide 2: Motivation
IBPSA offers essentially two heat pump models
  Carnot (y and TCon)
  WaterToWater (Scroll and Reciprocating)
IBPSA offers essentially one chiller model
  Carnot (y and TCon)
Central technology for energy transition  IBPSA should offer more options
Options
  Different sinks and sources (air, water, brine, …)
  Different sizes (small and large scale)
  Different model approaches (White, Gray, Black-box)
  Devices can be reversible, act as one another (currently not offered at all)
Modular reversible approach to have one model interface (parameters, assumptions, …) but flexible model options

## Slide 3: How the model looks IBPSA.Fluid.HeatPumps.BaseClasses.PartialReversibleVapourCompressionMachine
Different Options

## Slide 4: How the model looks IBPSA.Fluid.HeatPumps.BlackBoxData
Heat pump approaches
  Carnot
  European Data 2D and 3D (EN 14511)
  ASHRAE tbd.
  VCLib (validated stationary performance map)  SDF Problem
Chiller approaches
  Carnot
  European Norm 2D (EN 14511)
  ASHRAE tbd.
Discussion: Is BlackBoxData fitting?
  Carnot or VCLib are purely physical models, i.e. white-box
  To the system level, the models are I/O, i.e. black-box
  What could be a better name?
Discussion: Is “revSet” fitting?
  Prior: ModeSet for mode of heat pump
  Currently: ReverseSet  Not Backwards compatible
RefrigerantCycle
coo and hea

## Slide 5: Current status
Mayor changes compared to AixLib
  Different naming
  Easy parameterization
  No external bus connector (still available for libraries if wanted)  Merge scripts to be adjusted
  Several fixes to be compatible to OpenModelica
  Added carnot models instead of functions
  …
Open points
  Finalize Examples for heat pumps  On/Off enough?
  Create Examples for chillers
  Write Documentation
Discussion: What to delete
  TSet option (would require even more examples  tbd. in a later issue
  SDF option  Requires SDF option in MSL (https://github.com/modelica/ModelicaStandardLibrary/issues/1153)
In later issue
Provide speed comparison